| Producer | Measurement | Data Type | Production Volume (Bytes) | Production Speed | Expected Accuracy | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| AB-BDI | Total beam intensity | protons | 8 | 1 sec | 1% |  |
| AB-BDI | Individual bunch intensities | protons | 28,512 | 1 min | 5% |  |
| AB-BDI | Average 2D beam size | mm | 16 | 1 sec | 15% | For transport to IP will require knowledge of beta function |
| AB-BDI | Individual 2D bunch size | mm | 44,928 | 1 min | 15% | For transport to IP will require knowledge of beta function |
| AB-BDI | Average bunch length | ps | 8 | 1 sec | 1% |  |
| AB-BDI | Total longitudinal distribution |  | 285,120 | 1 min |  | Will be able to detect ghost bunches at the 0.1% level of nominal |
| AB-BDI | Average HOR & VER positions | um | 32 | 1 sec | 50um | From the BPMs located at Q1 either side of each IP |
| AB-BDI | Luminosity |  | 28,512 | 10 sec | 1% relative | This is a relative measurement between bunches |
| AB-BDI | Beam Loss |  |  |  |  | Which Monitors? Bunch by bunch? |